## Slide 1: Demo preparation
Connect Raspberry Pi and access point to power – requires a 2A power adapter minimum!!!!
Connect Laptop to acces point ‘devices’, password as printed on device
Open browser, http://tplinkwifi.net or 192.168.0.1
Log-in with username and password as printed on device
Navigate to ‘Wireless’
In Client Settings configure customer network SSID and Password
Navigate to ‘DHCP’ -> ‘DHCP Client List’ to find IP addresses of connected devices
Connect Pi to projector using HDMI
Connect to Pi using SSH ‘pi@192.168.0.10x’, standard password

## Slide 2: Demo
Issue ‘workon cv’ in command line
Change Directory ‘cd Development’
Run ‘python predict_model.py‘ for inference
Run ‘python cam_preview.py‘ to preview image on projector
Run python predict_model.py –img ‘cat.jpg‘ to send existing image to model

## Slide 3
Christian Petters, Solutions Architect
MXNet on Edge
with Raspberry Pi
Saturday, July 28, 2018
Notes: Challenges:
Having ML models doesn’t make an AI company
ML needs to be integrated in infrastructure ecosystem and business processes
ML code is only a small part of an overall ML production system
Old and new challenges for development and support processes
Operational requirements around model governance and auditability

## Slide 4: Deep Learning challenges at the Edge
Resource-constrained devices
  CPU, memory, storage, power consumption.
Network connectivity
  Availability, cost, bandwidth, latency.
  On-device prediction may be the only option.
Deployment
  Updating code and models on a fleet of devices is not easy.

## Slide 5: Good prediction performance at the Edge
MXNet is written in C++.
Gluon networks can be ‘hybridized’ for additional speed.
Two libraries boost performance on CPU-only devices
  Fast implementation of math primitives
  Hardware-specific instructions, e.g. Intel AVX or ARM NEON
  Intel Math Kernel Library https://software.intel.com/en-us/mkl
  NNPACK https://github.com/Maratyszcza/NNPACK
Mixed precision training
  Use float16 instead of float32 for weights and activations
  Almost 2x reduction in model size, no loss of accuracy, faster inference
  https://devblogs.nvidia.com/parallelforall/mixed-precision-training-deep-neural-networks/

## Slide 6: Demo time

## Slide 7: MXNet compilation from source on Raspberry Pi
Install dependencies
  sudo apt-get update
  sudo apt-get -y install git cmake build-essential g++-4.8 c++-4.8
  sudo apt-get liblapack* libblas* libopencv*
Clone source repository
  git clone https://github.com/apache/incubator-mxnet.git --recursive
Build MXNet library
  cd incubator-mxnet
  export USE_OPENCV=0
  make

## Slide 8: MXNet compilation from source on Raspberry Pi
Compilation duration
  Compilation on Raspberry Pi takes hours
Common issue
  Compiler running out of memory
    Edit /etc/dphys-swapfile, set CONF_SWAPSIZE=1024
    Run sudo /etc/init.d/dphys-swapfile restart
Reference
  https://aws.amazon.com/blogs/machine-learning/build-a-real-time-object-classification-system-with-apache-mxnet-on-raspberry-pi/
  Also includes additional steps to connect to Amazon IoT